## Slide 1: GridLAB-D Tutorial
David P. Chassin
Fall 2016
dchassin@slac.stanford.edu
Copyright © 2016, SLAC National Accelerator Laboratory
All registered trademarks are hereby recognized.
Short Course

## Slide 2: Tutorial objectives
Instruct on GridLAB-D
  Using the simulation
  Creating new models
Addresses the following topics
  Using the GridLAB-D modeling (GLM) language
  Creating models, running simulations, and extracting results
Not included
  Administering, configuring, and optimizing GridLAB-D systems
  Creating large-scale GridLAB-D operating environments
  Programming and debugging with GridLAB-D
  Installation and maintenance
  Powerflow, residential, generators and climate modules

## Slide 3: What to expect
Does not address the following topics:
  How to integrate or link GridLAB-D with other simulations
  How to change how GridLAB-D works internally
You will need the following to complete exercises:
  A system on which to install GridLAB-D (Windows 64, RHEL-6, or Mac OSX Mavericks or Yosemite)
  Install GridLAB-D from https://github.com/dchassin/gridlabd
  Development tools (e.g., git, autotools, gcc/mingw, gdb, lldb)
  Install Matlab and MySQL
  Material written for Eclipse users, but this is not required
  Optional tools include (e.g., gnuplot) not used in this course.
Note regarding GridLAB-D Version
  Material includes features only supported as of Version 4.0

## Slide 4: Course outline
Introduction and fundamentals
Getting help online
Data input and output
Linking to Matlab
Runtime classes
Realtime simulation

## Slide 5: Tutorial structure
Topic Instruction
  Objectives
  Theory and concepts
  Methods and applications
  Worked examples
Exercises
  Problems to solve
  Solutions available at https://github.com/dchassin/tutorial

## Slide 6: What is GridLAB-D?
Background on what GridLAB-D
does and how it does it.

## Slide 7: Agent-based simulations
What does agent-based mean?
  Changing states of each device is modeled independently
  Interactions between individuals are captured
  Environment in which agents evolve emerges from interactions
Examples:
  Social sims (e.g., Repast, Swarm)
  Computational economics (e.g., AMES)
  Engineered systems (e.g., TRANSIM)
Not examples:
  Simcity (it’s cellular automaton-based simulation)
  Flight simulator (it’s a model-based simulation)
  EPRI DSS (implementation of an algebraic solution)
  Any stochastic simulation/model

## Slide 8: Notional Example: Lotka-Volterra system
Predator-prey population dynamics
Simulations can be one of
Static – model equilibrium point
Dynamic – model one trajectory
External influences
New equilibrium
New trajectory
Simulation considerations
Series of steady states
Transient dynamics

## Slide 9: Numerical simulation error
Finite difference error
Agent-based error

## Slide 10: GridLAB-D simulation method
Time-series of steady states of resolution x
with variable time-step of resolution t
Time (t)
State (x)
x
t

## Slide 11: Determining next state change
Resolution of multiple overlapping time series
Time (t)
State (x)

## Slide 12: Caveats
Iterations are often required to find next state
  Non-strictly causal behavior is allowed
No guarantee of convergence
  Non-causal behavior is not prohibited
  Multiple simultaneous interacting models
  Incomplete information exchange
  Presence of integral/discrete state variables
Numerous layers of interaction
  Makes diagnostics difficult
  Can lead to unintended consequences

## Slide 13: GLM Files
GLM files describe simulations
  Input files (GridLAB-D Model)
  Classes, objects, players, recorders and clocks
Strengths
  Relatively easy to read and edit
  Rich parametric syntax for managing multiple models
  Single object definition can become entire populations
  Object properties can have distributions
Weaknesses
  Not directly compatible with any major software tools
  Integration modules/tools have been developed

## Slide 14: What is a GLM File?
Declares classes to use
  Standard classes are implemented in modules
  All classes can be extended at runtime
  New classes can be defined at runtime
Defines overall model structure
  Establishes initial conditions
  Defines certain boundary conditions
  Determines starting time and stopping conditions
Constructs inputs and outputs objects
  Players, recorders, collectors are objects too
Notes: Model your own system at the end of the class.
Adding regulators to manage the system
What are the benefits of doing this.
Different type of control schemes
What are the effects of smart meter (price on demand meter), how much does the utitily has to bear.
benefits to customer
profits are less to utility at peak times

## Slide 15: What is a module?
Collects classes that are related
  Delivers all model functionality related to a particular domain
  Loaded on demand
  Groups common parameters and domain solvers
  Often include module globals to control features
May be proprietary or open-source
  Most modules are downloads from SourceForge
  Vendor-based distributions possible

## Slide 16: Modules Available
Climate (incorporates weather data)
Buildings
  Commercial (single-zone office buildings) – in progress
  Residential (HVAC and appliance models)
Electrical network
  Powerflow (3 phase unbalanced distribution solver – FBS/NR)
  Reliability (events, metrics)
  Distributed Generators (battery, diesel, PV, wind, inverters) – generalized models – further development this year
Markets
  Double and single sided auctions
  Appliance controllers
Input/Output
  Players, recorders, collectors, MySQL, Matlab

## Slide 17: Describing models: classes
Classes define similar objects
  Properties are the same for all objects
  Behavior are can be set parametrically
  Exposed methods (if any) are shared
Static classes are precompiled in modules
  Hard to build but very rich and detailed
Runtime classes are user-defined
  Easier to build but harder to make detailed
  Detail is limited by code size and data exchange library
Notes: Real examples. Explain to me more about this.

## Slide 18: Describing systems: objects
Objects are instances of classes
  Single instance or population of instances
Object properties
  Simple value or distribution of values
Parent-child relation
  Primary solver dependency relationship
  Child dependent on parent before parent dependent on child
  Parent expected to aggregate information from children

## Slide 19: Example Object Declaration
Define a house with default values
  module residential; // module declaration
  object house { // instantiation of an object of class house
  name MyHouse; // name the new object
  }
Define a house with custom values
  module residential;
  #include "CA-Los_angeles.glm“ // load weather
  object house {
  name MyHouse;
  floor_area random.normal(1500,300) sf; // random initial value
  heating_setpoint 70.0 degF; // heating setpoint
  cooling_setpoint 76.0 degF; // cooling setpoint
  thermostat_deadband 1.0 degF; // thermostat hysteresis
  }

## Slide 20: Controlling time: clocks
System clock represents simulation time
  Objects have private synchronization clock
  Clock time resolution is 1 sec or greater
  Cannot represent any time before TS_INIT
  TS_INIT is Jan 1, 1970 0:00:00 UTC
Local time based on time zones
  Use POSIX standard (e.g., PST+8PDT)
  Alternative localization (e.g., US/CA/San Francisco)
Summer (daylight savings) time rules are handled
  Summer time rule change years are supported

## Slide 21: Clock
Establish the simulation time range for the model
clock {
timezone PST+8PDT;
starttime '2000-01-01 0:00:00 PST';
stoptime '2001-01-01 0:00:00 PST';
}

## Slide 22: Example of GLM file
  clock {
  timezone PST+8PDT;
  starttime '2000-01-01 0:00:00 PST';
  stoptime '2000-07-01 0:00:00 PST';
  }
  module residential;
  object house {
  floor_area random.normal(1500,300) sf;
  heating_setpoint 70.0 degF;
  cooling_setpoint 76.0 degF;
  thermostat_deadband 1.0 degF;
  }

## Slide 23: Running Simulations
Details on how to run and control
GridLAB-D models

## Slide 24: Specifying input file
To run a GLM file
  Command line must point to location of the executable
  host% gridlabd run_file.glm

## Slide 25: Saving output
Output by default goes to current executable location
  Only saves final state of the system
Sending output to another file
host% gridlabd file1.glm -o file1.xml
  Saves the instance this run created
Be careful not to overwrite input file
host% gridlabd file1 -o file1.glm (BAD!)

## Slide 26: Controlling output messages
Warnings can be disabled
host% gridlabd --warn file1.glm
Verbose output can be enabled
host% gridlabd --verbose file1.glm
Debug messages can be toggled
host% gridlabd --debug file1.glm
Quiet suppresses almost all messages
host% gridlabd --quiet file1.glm

## Slide 27: Controlling global parameters
Many parameters have global or module scope
  Custom model parameters also allowed
Parameters are defined as model globals
host% gridlabd –D name=value file1.glm
Modules can also have their own globals
host% gridlabd –D module::name=value file1.glm
  (More about this when using GLM macros)

## Slide 28: Some useful global variables
iteration_limit | Maximum number of iterations allowed before convergence fails (default=100)
dumpfile | File to use for model dump if simulation fails (default=gridlabd.xml)
stoptime | Simulation time at which to stop regardless of state (default=never)
kmlfile | Google Earth output file (default=gridlabd.kml)
urlbase | URL base for stylesheets when viewing XML files in a browser (default=http://www.gridlabd.org)
timezone | The default timezone to use if non specified in the model (default=locale)
randomseed | Deterministic pseudo-random number seed; 0 means non-deterministic random numbers (default=0)

## Slide 29: Reading error messages
Loader messages
  file.glm(line): load message
Compiler messages
  file.glm(line): cpp message
  -or-
  file.cpp(line): cpp message
Simulator runtime messages
  ERROR[timestamp]: exec message

## Slide 30: Configuration files
gridlabd.conf
  System copy is in /usr/local/share/gridlabd folder
  A local copy will override system copy
  Has system-wide settings
  Must be valid for all users
gridlabd-user.conf
  User-specific settings
  Based on USER or USERNAME environment variable
  Can be loaded /usr/local/share/gridlabd configuration file

## Slide 31: Questions?

## Slide 32: Getting Help
How to get help and report problems.

## Slide 33: Help Resources
Runtime resources
  --help, --modhelp module[:class]
Troubleshooting pages
  Documents warning and error messages
SF Wiki
  Latest documentation
  Searchable and you can make edits (registered users)
SF Forums
  Questions not covered by Wiki
  All users see answer
SF user emails
  Ok, but not always as quick
  Other users don’t benefit from answer
SF TRAC
  Used if none of the above addresses the problem
  Used to report “bugs” or requested upgrades

## Slide 34: Command line: --help
host% gridlabd --help
Syntax: gridlabd [<options>] file1 [file2 [...]]
Command-line options
--------------------
--check|-c Performs module checks before starting simulation
--debug Toggles display of debug messages
--debugger Enables the debugger
--dumpall Dumps the global variable list
--mt_profile <n-threads> Analyses multithreaded performance profile
--profile Toggles performance profiling of core and modules while simulation runs
--quiet|-q Toggles suppression of all but error and fatal messages
--verbose|-v Toggles output of verbose messages
--warn|-w Toggles display of warning messages
--workdir|-W Sets the working directory
Global and module control
-------------------------
--define|-D <name>=[<module>:]<value> Defines or sets a global (or module) variable
--globals Displays a sorted list of all global variables
--libinfo|-L <module> Displays information about a module
Information
-----------
--copyright Displays copyright
--license Displays the license agreement
--version|-V Displays the version information
--setup Open simulation setup screen
...

## Slide 35: Command line: --modhelp tape:player
host% gridlabd --modhelp tape:player
module tape {
char1024 gnuplot_path;
int32 flush_interval;
int32 csv_data_only;
int32 csv_keep_clean;
timestamp delta_mode_needed;
}
class player {
char256 property;
char1024 file;
char8 filetype;
char32 mode;
int32 loop;
}

## Slide 36: Command line: --modhelp
host% gridlabd --modhelp powerflow:line
module powerflow {
bool show_matrix_values;
double primary_voltage_ratio;
double nominal_frequency;
bool require_voltage_control;
double geographic_degree;
complex fault_impedance;
double warning_underfrequency;
double warning_overfrequency;
double warning_undervoltage;
double warning_overvoltage;
double warning_voltageangle;
double maximum_voltage_error;
enumeration {NR=2, GS=1, FBS=0} solver_method;
bool line_capacitance;
bool line_limits;
char256 lu_solver;
int64 NR_iteration_limit;
int32 NR_superLU_procs;
double default_maximum_voltage_error;
double default_maximum_power_error;
bool NR_admit_change;
bool enable_subsecond_models; // Enable deltamode capabilities within the powerflow module
bool all_powerflow_delta; // Forces all powerflow objects that are capable to participate in deltamode
double deltamode_timestep[ns]; // Desired minimum timestep for deltamode-related simulations
int64 deltamode_extra_function;
double current_frequency[Hz]; // Current system-level frequency of the powerflow system
bool master_frequency_update; // Tracking variable to see if an object has become the system frequency updater
bool enable_frequency_dependence; // Flag to enable frequency-based variations in impedance values of lines and loads
double default_resistance;
bool enable_inrush; // Flag to enable in-rush calculations for lines and transformers in deltamode
double low_voltage_impedance_level; // Lower limit of voltage (in per-unit) at which all load types are converted to impedance for in-rush calculations
char1024 market_price_name;
}
...
Notes: What is the purpose of this slide?

## Slide 37: Command line: --modhelp
host% gridlabd --modhelp powerflow:line
class line {
parent link;
class link {
parent powerflow_object;
class powerflow_object {
set {A=1, B=2, C=4, D=256, N=8, S=112, G=128} phases;
double nominal_voltage[V];
}
function interupdate_pwr_object();
function update_power_pwr_object();
function check_limits_pwr_object();
enumeration {OPEN=0, CLOSED=1} status; //
object from; // from_node - source node
object to; // to_node - load node
complex power_in[VA]; // power flow in (w.r.t from node)
complex power_out[VA]; // power flow out (w.r.t to node)
double power_out_real[W]; // power flow out (w.r.t to node), real
complex power_losses[VA]; // power losses
complex power_in_A[VA]; // power flow in (w.r.t from node), phase A
complex power_in_B[VA]; // power flow in (w.r.t from node), phase B
complex power_in_C[VA]; // power flow in (w.r.t from node), phase C
complex power_out_A[VA]; // power flow out (w.r.t to node), phase A
complex power_out_B[VA]; // power flow out (w.r.t to node), phase B
complex power_out_C[VA]; // power flow out (w.r.t to node), phase C
complex power_losses_A[VA]; // power losses, phase A
complex power_losses_B[VA]; // power losses, phase B
complex power_losses_C[VA]; // power losses, phase C
complex current_out_A[A]; // current flow out of link (w.r.t. to node), phase A
complex current_out_B[A]; // current flow out of link (w.r.t. to node), phase B
complex current_out_C[A]; // current flow out of link (w.r.t. to node), phase C
complex current_in_A[A]; // current flow to link (w.r.t from node), phase A
complex current_in_B[A]; // current flow to link (w.r.t from node), phase B
complex current_in_C[A]; // current flow to link (w.r.t from node), phase C
complex fault_current_in_A[A]; // fault current flowing in, phase A
complex fault_current_in_B[A]; // fault current flowing in, phase B
complex fault_current_in_C[A]; // fault current flowing in, phase C
complex fault_current_out_A[A]; // fault current flowing out, phase A
complex fault_current_out_B[A]; // fault current flowing out, phase B
complex fault_current_out_C[A]; // fault current flowing out, phase C
set {CN=768, CR=512, CF=256, BN=48, BR=32, BF=16, AN=3, AR=2, AF=1, UNKNOWN=0} flow_direction; // flag used for describing direction of the flow of power
double mean_repair_time[s]; // Time after a fault clears for the object to be back in service
double continuous_rating[A]; // Continuous rating for this link object (set individual line segments
double emergency_rating[A]; // Emergency rating for this link object (set individual line segments
double inrush_convergence_value[V]; // Tolerance, as change in line voltage drop between iterations, for deltamode in-rush completion
}
function interupdate_pwr_object();
function update_power_pwr_object();
function check_limits_pwr_object();
object configuration;
double length[ft];
}
Notes: What is the purpose of this slide?

## Slide 38: Command line: --example
host% gridlabd --example climate:climate
object climate:0 {
// header properties
rank 0;
clock (invalid);
flags NONE;
// climate properties
solar_elevation +0;
solar_azimuth +0;
solar_zenith +0;
city "";
tmyfile "";
temperature +0 degF;
humidity +0 pu;
solar_flux +0 W/sf;
solar_direct +0 W/sf;
solar_diffuse +0 W/sf;
solar_global +0 W/sf;
extraterrestrial_global_horizontal +0 W/sf;
extraterrestrial_direct_normal +0 W/sf;
pressure +0 mbar;
wind_speed +0 m/s;
wind_dir +0 deg;
wind_gust +0 mph;
record.low +0 degF;
record.low_day 0;
record.high +0 degF;
record.high_day 0;
record.solar +0 W/sf;
rainfall +0 in/h;
snowdepth +0 in;
interpolate NONE;
solar_horiz +0;
solar_north +0;
solar_northeast +0;
solar_east +0;
solar_southeast +0;
solar_south +0;
solar_southwest +0;
solar_west +0;
solar_northwest +0;
solar_raw +0 W/sf;
ground_reflectivity +0 pu;
reader "";
forecast "";
cloud_model NONE;
cloud_opacity +0 pu;
opq_sky_cov +0 pu;
cloud_reflectivity +0 pu;
cloud_speed_factor +0 pu;
solar_cloud_direct +0 W/sf;
solar_cloud_diffuse +0 W/sf;
solar_cloud_global +0 W/sf;
cloud_alpha +0 pu;
cloud_num_layers +0 pu;
cloud_aerosol_transmissivity +0 pu;
}

## Slide 39: Command line: --info <topic>
Searches wiki pages for the topic
host% gridlabd --info "Getting help"

## Slide 40: Online help resources

## Slide 41: SourceForce MediaWiki

## Slide 42: Help Guides

## Slide 43: Topic Index

## Slide 44: Forum

## Slide 45: Posting to the forum

## Slide 46: Troubleshooting

## Slide 47: Troubleshooting

## Slide 48: Questions?

## Slide 49: Modeling language basics
Detailed discussion of GridLAB-D modeling language (GLM).

## Slide 50: Top-level Directives
Instructs loader on the content of the next GLM block
  clock – controls time
  module – loads groups of classes and functions
  class – defines a class
  object – defines an object
  import – imports a model
  export – exports a model
  link – links a model to an external tool
  filter – defines a filter to connect object properties
  extern – defines a function to connect object properties

## Slide 51: Clock directive
clock {
timezone PST+8PDT;
starttime '2001-01-23 01:23:45 PST';
stoptime '2001-06-12 01:23:45 PDT';
}
Specifies the timezone (must come first)
Sets the start time
Sets the end time (if steady state not reached first)

## Slide 52: Module directive
module powerflow {
solver_method NR;
NR_iteration_limit 50;
}
Loads the named module
Sets the module’s variables (overrides default)
Modules define one or more classes
Modules often come with other functions

## Slide 53: Class directive
class house {
double floor_area[sf];
}
Asserts structure of an existing class
  Load fails if actual structure does not match
Add new variables to an existing class
  Type, name and units are defined.
Can be used to create a new class
  Must include init and sync (more on this later)
  (Windows users must installed mingw)

## Slide 54: Property types
bool
char8, char32, char256, char1024
int8, int16, int32, int64, timestamp,
enumeration, set
double, complex, float, real, randomvar, double_array,
loadshape, enduse, object

## Slide 55: Example property values
  is_enabled TRUE; // boolean
  motor_state STALLED; // set/enumeration
  city "Richland"; //char*
  start_at '2008-04-01 12:00:00 PDT'; // timestamp
  floor_area 2000; // double
  floor_area 250 m^2; // double with units
  floor_area random.triangle(1500,2500); // functional
  wall_area (sqrt($var)*8); // calculated
  name `{class}:{id}`; // expansion
  name ${var++}; // expression
  test_result (test_value) ? "<=0" : ">0"; // trinary

## Slide 56: Property units
Defines how values are stored in memory
  Double and complex converted automatically
General unit conversion system used
  Standard units (m, W, V, A, h, s)
  Conventional units (kW, kVA, Btu)
  Derived units (e.g., MW/h)—beware of quirks
  Complete list of units in unitfile.txt
  If unit is not define the value is dimensionless
  If unit is not specified the property’s unit is assumed

## Slide 57: Reserved property names
Used by object headers
Cannot be used in class definitions
class invalid {
object parent;
}
Can be set in object definitions
object dryer {
parent my_house;
}
parent
rank
clock
valid_to
latitude
longitude
in_svc
out_svc
flags

## Slide 58: Object directive
Basic syntax
    object classname {
    property_name value;
    ...
    }
Defining multiple objects at once
    object class:..count ...
Numerical identifiers
    object class:num ...
    object class:first..last ...

## Slide 59: Rules for values
Double quotes required if string has spaces
  Non-string values are converted automatically
  Quotes suppress all other rules (math, expansions, etc.)
Times and other special types
  Requires single quotes when spaces are included
Functional values allowed outside parentheses
  random.dist(args...)
Some properties use extended syntax, e.g.,
  my_randomvar "type:normal(0,1); min:0; refresh:30s;";

## Slide 60: Expression syntax
Standard math operations used
    ((12+8)/9)
Usual math functions supported
    (sin((12+8)/2*Pi))
Can refer to other properties of object, e.g.,
    (… $property_name …)
    (… this.property_name …)
    (… parent.property_name …)
    (… object.property_name …)  caveat!

## Slide 61: Functionals
Only for random numbers
Distributions require arguments
Discrete distributions
  degenerate(x)
  bernoulli(p)
  sampled(n,x1,x2,…,xn)
Others likely coming
Continuous distributions
  uniform(a,b)
  normal(m,s)
  lognormal(m,s)
  exponential(l)
  pareto(m,g)
  beta(a,b)
  gamma(a,b)
  weibull(l,k)
  rayleigh(s)
  triangle(a,b)

## Slide 62: Nested objects
Implicit parent-child relationship
Allows generation of population
Avoid having to provide names
Equivalent:
    object house { object house {
    object dryer { name my_house;
    ... ...
    }; }
    ... object dryer {
    } parent my_house;
    ...
    }
No equivalent: object house:..10

## Slide 63: Macro processing
Hash (#) in first non-white of a line specifies macros
Macro processing is done first
New values stored as global variables
#define MYDEF=text
Inline substitutions of macros syntax
  ${MYDEF}
Environment variables also substituted
  ${USER}

## Slide 64: Standard macros
Standard expressions
  #include filename
  #print expression
  #warning message
  #error message
  #define name=value
  #set name=value
  #setenv name=value
Conditionals
  #if expression
  #else
  #endif
  #ifdef name
  …
  #ifndef name
  …
  #ifexist file
  …

## Slide 65: Schedules, Loadshapes, and Enduses
schedule directive is available
  Provides efficient built-in support for recurring values
Loadshape property
  Reads a schedule to update load
  Implements various typical load behaviors
Enduse property
  Reads loadshape
  Synthesize power demand

## Slide 66: Questions?

## Slide 67: Data Input and Output
Introduce objects that control flow of data in and out of GridLAB-D.

## Slide 68: Extracting final results: XML dump
XML files describe models
  Classes, objects, players, recorders and clocks
Strengths
  Highly compatible with other software
  Faithful representation of a single model instance
Weaknesses
  Viewing and editing only with third-party tools
  Rigid (non-parametric) syntax
  Not good for creating large complex models
  No populations or distribution allowed
  Not easily used for extraction of time series data

## Slide 69: Extracting intermediate results
Recorders
  Samples a single object’s properties at designated times
  Handles unit conversion if unit is specified
  Samples stored in file or database (depends on module)
  Triggers can start recording conditionally
  Limits can end recording conditionally
Multi-recorder
  Multi-object variant records several objects
Collector
  Aggregates samples (e.g., mean, stdev, min, max, etc.)
Histogram
  Counts samples in bins, saves and reset at intervals

## Slide 70: Introducing data
Players
  Alter object properties at designated times
  Used to alter boundary conditions
  Can use relative time and looped
Shapers
  Schedules (using POSIX cron standard)
  Amplitude: copies value directly
  Pulse-width: on/off with a probability
  Queues: accrues to threshold before “on”

## Slide 71: Tape Module
Changing properties
  Player
  Shaper
Sampling properties
  Recorder
  Multi_recorder
  Collector
  Histogram
  Group_recorder
  Violation_recorder
MySQL Module
  Database
Mimics tape module
  Player
  Recorder
  Collector

## Slide 72: Internal data sources and links
Schedules
  Represent periodic data (minute, hour, day, month, weekday)
  More efficient than player or shaper objects
  Preloaded into core memory on initialization
  Often used in conjunction with loadshape and enduse
Transforms
  Defines reusable functions to transform a source property and apply it to a destination property
Filter
  Defines a reusable discrete-time digital filter to transform a source property and apply the result to a destination property

## Slide 73: MySQL module
Implements same functionality as tape module
Global variables for mysql module:
  module mysql {
  hostname "localhost";
  username "gridlabd";
  password "";
  schema "gridlabd";
  port 3306;
  socketname "/tmp/mysql.sock";
  }

## Slide 74: Database object
Used by other objects to make queries
  Specify server access/protocol
  Specify default behaviors and options
Multiple database objects allowed
  If multiple used, each object must specify database to use
Options:
  NOCREATE: disables automatic table creation
  NEWDB: destroys old schema before starting simulation
  OVERWRITE: destroys old data before writing new data

## Slide 75: Database object properties
  object database {
  hostname "localhost";
  username "gridlabd";
  password "";
  schema "gridlabd";
  port 3306;
  socketname "/tmp/mysql.sock";
  options SHOWQUERY|NOCREATE|NEWDB|OVERWRITE;
  on_init file-name;
  on_sync file-name;
  on_term file-name;
  sync_interval seconds;
  tz_offset seconds;
  uses_dst FALSE;
  }

## Slide 76: Players
object player {
property property-name;
table source-table;
connection database-object-name;
loop number-of-loops;
}
Syntax compatible with tape:player
  “file”  “table”
  “mode” and “filetype” are ignored

## Slide 77: Recorders
Target object is parent (if specified)
  If absent, all properties my use specify object name
Table name (aka, “file”)
  Multiple objects can use same table (must have same fields)
Property list
  Multiple fields allowed (comma separated)
  Object name allowed (e.g., “name.property”)
Special fields
  Record id, default is “id”
  Timestamp, default “t”
  Header fields (name, class, latitude, longitude), default is “”

## Slide 78: Collectors
object collector {
property property-name;
group group-spec;
table|file source-table;
mode {"w","w+","a","a+"};
limit max-rows;
interval seconds;
connection database-object-name;
options PURGE;
}

## Slide 79: Summary
Player and Shaper
  Used to update information at a specific time from a file
Recorder and Collector
  Used to collect information from the model
  Can also plot to screen or file (tape only)
Loadshapes and Schedules
  NOT part of the tape module, but similar functionality
  Updates recurring information at a specific time directly from the core (not from a file)
Transforms and Filters
  Uses data from a source variable to modify other properties

## Slide 80: Players
Objects that set and control the boundary conditions.

## Slide 81: Input object: player
Implemented in tape and mysql modules
  One of three primary ways of inputting data
  Tapes apply a time-series to a single property of the parent object
Several possible sources of tape data
  File : source is a CSV files
  ODBC : source is a database
  Memory : source is a global variable
  MySQL : source is a table

## Slide 82: Player timestamps
Timestamp is the beginning of interval
  Absolute time uses ISO time format
  YYYY-MM-DD hh:mm:ss [ZZZ]
  Missing timezone implies UTC (not local timezone!)
  Relative times use “+” prefix, e.g., “+600”
  Relative times can have units (default is seconds)
  “s”, “m”, “h”, “d”, “w”,
  Examples: +12h
Warning: “m” is not the standard unit for minutes. The tape modules does not use GridLAB-D’s unit conversion system, in which the standard unit for a minute is “min”.

## Slide 83: Player “property”
Name of parent’s property that is updated
Data conversion is automatic
  Conversion is from text input
  Boolean uses TRUE or FALSE and/or 0 or 1
  Integer uses atoi()
  Enumeration/set uses keywords (specific to property)
  Double uses double_format (a global variable)
  Complex uses complex_format (a global variable)
  Object references use object_scan format (global)
Warning: Tape player does not support units but mysql player does.

## Slide 84: Player “file”
Determines the source CSV file of the data
  Require that file property be the filename
  Format is CSV, but others may be coming
Directory delimiter can be system specific
  “/” are normally used; “\” allowed in Windows
Meaning differs based on filetype property
  Default is “txt”
  “odbc” is for databases: file is connection string
  “memory” is for Matlab data: file is global variable name
  Not supported in mysql player

## Slide 85: Player “loop”
Indicates how many times the data source is to be read
  Default (0) is to not loop
Absolute timestamps are read only on first pass
Relative time offsets are used on all passes

## Slide 86: Example player object
object house {
floor_area random.normal(1500,300);
object player {
property air_temperature;
file "tair.csv”
loop 10;
};
}

## Slide 87: Example player file
# comment lines start with hash sign
# this example will produce a square wave timeseries
# alternating every hour between 72 and 73
# this is an absolute timestamp
# it is read only on the first pass
2007-01-01 00:00:00, 72.0
# these are relative timestamps
# they are read on every pass
+1h, 73.0
+1h, 72.0

## Slide 88: Another Example
Another way to code
  object house:1 {
  floor_area random.normal(1500,300);
  }
  object player {
  parent house:1
  property air_temperature
  file "tair.csv";
  loop 21;
  }

## Slide 89: Yet another Example
Another way to code
  object house {
  name MyHouse1;
  floor_area random.normal(1500,300);
  }
  object player {
  parent MyHouse1;
  property air_temperature
  file "tair.csv";
  loop 21;
  }

## Slide 90: Another example player file
# comment lines start with hash sign
# this example will produce a time series of
# temperatures for midnight-3 am, then stay at
# 68.0 degrees indefinitely
2007-01-01 00:00:00, 72.0
2007-01-01 01:00:00, 73.0
2007-01-01 02:00:00, 72.0
2007-01-01 03:00:00, 68.0

## Slide 91: Demo
Manipulate thermostatic controls using player: player.glm
    clock {
    timezone PST+8PDT;
    starttime '2001-01-01 00:00:00 PST';
    }
    module residential;
    module tape;
    object house {
    heating_setpoint 40 degF;
    cooling_setpoint 90 degF;
    object player {
    property cooling_setpoint;
    file theat.csv;
    loop 28;
    };
    }

## Slide 92: Demo
Another way to manipulate values using player: player_2.glm
    clock {
    timezone PST+8PDT;
    starttime '2001-01-01 00:00:00 PST';
    }
    module residential;
    module tape;
    object house {
    name MyHouse1;
    heating_setpoint 40 degF;
    cooling_setpoint 90 degF;
    }
    object player {
    parent MyHouse1;
    property cooling_setpoint;
    file theat.csv;
    loop 28;
    }

## Slide 93: Example player file: theat.csv
  2001-01-02 06:00:00,75
  +15h,60
  +9h,75
Note: Excel does not handle ISO date formats, timezones, or daylight savings time rules correctly. To avoid issues, use UTC time for all timestamps as much as possible.
Tip: In Excel use custom cell formats for timestamps:
yyyy-mm-dd HH:MM:SS
yyyy-mm-dd HH:MM:SS "PST"

## Slide 94: Player transforms
object class {
property source*scalar+offset;
}
Used to create a linear function of value
  y = m*x + b
  A single common input used by multiple objects
Easy offsets and scaling of shapes from a single source

## Slide 95: Player transforms
Created in multiple steps:
  // trick to publish the input value when no parent is set
  class player { // this only needs to be done once
  double value; // at the beginning of the glm file
  }
  object player { // this is only done once for each input
  name THeat;
  file theat.csv;
  loop 5;
  }
  object house:1 {
  heating_setpoint THeat.value*1+2; // syntax and order important
  }
  object house:2 {
  heating_setpoint THeat.value*1.1+4; // using different offset/scale
  }
This input can now be used by many objects

## Slide 96: MySQL player
Very similar to tape player objects
Requires database object to operate
  If none use, the default database is used
  Default database is specified by module declarations
  module mysql {
  hostname "localhost";
  username "gridlabd";
  password "";
  schema "gridlabd";
port 3306;
socketname "/tmp/mysql.sock";
clientflags COMPRESS|FOUND_ROWS|IGNORE_SIGPIPE|INTERACTIVE|LOCAL_FILES|MULTI_RESULTS|MULTI_STATEMENTS|NO_SCHEMA|ODBC|SSL|REMEMBER_OPTIONS;
}

## Slide 97: MySQL database
object database {
hostname "localhost";
username "gridlabd";
password "";
schema "gridlabd";
port 3306;
socketname "/tmp/mysql.sock";
clientflags COMPRESS|FOUND_ROWS|IGNORE_SIGPIPE|INTERACTIVE|LOCAL_FILES|MULTI_RESULTS|MULTI_STATEMENTS|NO_SCHEMA|ODBC|SSL|REMEMBER_OPTIONS;
options SHOWQUERY|NOCREATE|NEWDB|OVERWRITE;
on_init sql-script-name;
on_sync sql-script-name;
on_term sql-script-name;
sync_interval seconds;
}

## Slide 98: MySQL player
object player {
property property-name;
table|file source-table;
mode {"r","r+"};
filetype {"CSV"};
connection database-object-name;
options 0;
loop number-of-loops;
}

## Slide 99: Questions?

## Slide 100: Recorders
This section will introduce you to objects that record data in other objects.

## Slide 101: Output object
Implemented in tape and mysql module
  One of two primary ways of collecting data
  One of few objects which “drive” the simulation
  Recorders observe one or more properties of a single object
Several possible destinations for data (tape)
  File : source is a specially formatted files
  ODBC : source is a database
  Memory : source is a global variable
  Plot : gnuplot output

## Slide 102: Property
Name of parent’s property that is recorded
Internal data conversion is performed
  Conversion is to text output
  Booleans uses TRUE or FALSE and/or 0 or 1
  Integers use decimal integer
  Enumerations and set use keywords
  Doubles use double_format
    #set double_format=%.12lg allows user to modify format
  Complex uses complex_format
  Object references use object_format

## Slide 103: Property (cont.)
Unit conversion only performed if unit is specified
property name[unit];
  Example:
  object house {
  floor_area random.triable(1000,2000) sf;
  object recorder {
  property floor_area[m^2];
  // ...
  };
  }
Additional extensions used for complex numbers
  real, imag, mag, ang, arg
    property voltage_A.real;

## Slide 104: File
Meaning differs based on filetype property
  Format can be system specific
  “/” are normally used; “\” allowed in Windows
  File must be writeable
  Path to file is not automatically created
  Existing files are overwritten
Note: Write failure is not an error (simulation continues with a warning)

## Slide 105: Interval
Determines the sampling interval for data
  How often should I sample?
Units are seconds
  -1 means sample transients (on change)
  0 means sample each iteration
Interval “drives” simulation
  Affects numerical results if models don’t handle transients well
Note: recording samples are lagging (unlike players, which are leading)

## Slide 106: Limit
The maximum number of samples
  How many samples should I record?
Limits the size of the output file
  0 is default
  0 means no limit
Note: If a “stoptime” is not specified, simulation runs until all recorders reach their limits.

## Slide 107: Trigger
Specifies condition to start recording
  Works only for the target property
  Usual compare operations apply
  Once triggered, recording continues to limit
Example
  trigger "< 0"; // start recording when target is negative

## Slide 108: Multi-Recorder
Same basic syntax as a recorder
  Allows user to record from multiple objects into a single file
Example:
object meter {
name meter1;
phases ABCN;
nominal_voltage 7200;
object multi_recorder {
property "measured_real_power,meter2:constant_power_A_real";
limit 8808;
interval 1800;
file record_power.csv;
};
}
non-parent object

## Slide 109: Demo
// player_recorder.glm
module residential;
module tape;
clock {
timezone PST+8PDT;
starttime '2001-01-01 00:00:00 PST';
}
object house:1 {
heating_setpoint 40degF;
cooling_setpoint 90degF;
}
object player {
parent house:1;
property cooling_setpoint;
file theat.csv;
loop 100; // does not drive simulation
}
object recorder{
parent house:1;
property air_temperature,cooling_setpoint;
file theat_record.csv;
interval 7200; // 2 hours
limit 48; // records 48 samples -> drives simulation for 96 hours
}

## Slide 110: Demo
// player_recorder_interval.glm
    module residential;
    module tape;
    clock {
    timezone PST+8PDT;
    starttime '2001-01-01 0:00:00 PST';
    }
    object house:1 {
    heating_setpoint 40degF;
    cooling_setpoint 90degF;
    }
    object player {
    parent house:1;
    property cooling_setpoint;
    file theat.csv;
    loop 100;
    }
    object recorder{
    parent house:1;
    property air_temperature,cooling_setpoint;
    file theat_record_0.csv;
    interval 0; // sample each iteration (9pm and 6am from player)
    limit 48;
    }

## Slide 111: Example: intervals
// Interval -1, 0, 7200: player_recorder_trio.glm
  object player {
  parent house:1;
  property cooling_setpoint;
  file theat.csv;
  loop 100;
  }
  object recorder{
  parent house:1;
  property air_temperature,cooling_setpoint;
  file theat_record_7200.csv;
  interval 7200; // records every 2 hours for 48 x 2 hours
  limit 48;
  }
  object recorder{
  parent house:1;
  property air_temperature,cooling_setpoint;
  file theat_record_0.csv;
  interval 0; // records every iteration (9pm and 6am from player)
  limit 48;
  }
  object recorder{
  parent house:1;
  property air_temperature,cooling_setpoint;
  file theat_record_1.csv;
  interval -1; // record every change in value when clock advances
  limit 48;
  }

## Slide 112: Questions?

## Slide 113: Collectors
Objects that record aggregate data from groups of objects.

## Slide 114: Output object
Implemented in tape and mysql module
  One of two primary ways of recording data
  Same basic parameters as recorders
Collectors take aggregates of properties
  Observations collected from a group of objects
  Aggregations include statistics and min/max
  Aggregations are specified as part of property

## Slide 115: Group
Defines the subset of objects to observe
  Object properties used to define group
  Header properties allowed:
class, parent, rank, in_svc, out_svc, groupid
Search is performed only on first observation
  Search result is reused thereafter
  => Groups must be constant over time
  => Only time-invariant properties may be used in group criteria
Example: group "class=house";
  Can include multiple groupings
group "class=house AND groupid=feeder1"

## Slide 116: Property aggregators
Similar to recorders, but with aggregators
  count, min, max, avg, std, sum, prod
  mean, var, kur
  gamma
Parts used for complex values
  real, imag
  mag, ang, arg
Example: property "sum(power.mag)"

## Slide 117: Example
object collector {
group “class=house AND groupid=feeder1”;
property “sum(power.mag),avg(hvac_load.real)”;
interval 3600;
limit 24;
}

## Slide 118: Demo
// demo/collector.glm sum and average of the real power of light objects in houses
module residential{
implicit_enduses NONE;
}
module tape;
clock {
timezone PST+8PDT;
starttime '2001-01-01 0:00:00 PST';
stoptime '2001-07-01 00:00:00 PST';
}
schedule light_demand {
* 1-3 * * * 0;
* 4-6 * * * 0.15;
* 7-19 * * * 0;
* 20-0 * * * .85;
}
object house:..10 {
cooling_setpoint 90 degF;
object lights {
shape "type: analog; schedule: light_demand; power: 1.1 kW";
};
}
object collector {
file theat_collector.csv;
group "class=lights"; // sample only lights
property sum(energy.real),avg(energy.real); // use real part--aggregators need doubles
interval 3600;
limit 744;
}

## Slide 119: Questions?

## Slide 120: Exercises (players)
Create a player file that can be used to inject a daily heating setpoint. Nightime (72F) is 9PM to 6AM and daytime (75F) is 6AM to 9PM. Hint: use relative times.
Attach the player to a house and run the simulation for 4 weeks. Hint: you will need to loop the player file.
Modify Exercise 2 to create an additional home that uses a player transform to inject a daily heating setpoint. Nighttime (74F) is 9PM to 6AM and daytime (77F) is 6AM to 9PM.

## Slide 121: Exercises (recorders)
Create a recorder to collect hourly indoor air temperature of the default house for the year 2001.
Create a recorder to collect 100 values of the default waterheater power transitions (actual_load) in the default house.
Create a multi-recorder to record the waterheater power and the house HVAC power (hvac_load) at five minute intervals for one week.
Create two recorders to collect voltages in the IEEE 37 node test model (use load701 & node775; voltage_A, voltage_B, voltage_C) to observe the voltages as they converge. Hint: when using Excel, *.real and *.imag are very helpful.

## Slide 122: Exercises (collectors)
Collect total power consumption for a population of 100 water heaters for one month. Hint: use “actual_load”.
Collect the hourly mean, standard deviation, minimum and maximum indoor air temperature a population of 100 default houses for a week. Hint: use “air_temperature”.
Collect the minimum and maximum voltages of all nodes in the IEEE 37-bus test model as it converges. Hint: use voltage_A.mag, voltage_B.mag, & voltage_C.mag

## Slide 123: Connecting to Matlab

## Slide 124: Matlab "link" directive
GLM File:
link filename;
object class {
name name;
property-1 value-1;
property-2 value-2;
}
Link File:
target matlab
export name.property1 property1
import name.property2 property2
GridLAB-D Model
Matlab Workspace
Exports
Imports

## Slide 125: Import/Export properties
Mapping must be specified for each property
{import|export} object.property matlab-name
Import/export operation is done during "sync"
  Exports done first
  Matlab "sync" called (if any)
  Imports done last
Data types mapped automatically
  All properties mapped to double or complex
  Data type must be compatible

## Slide 126: Matlab Workspace
Root structure: "gridlabd" by default
  Can be named if "root" used
Globals variables
  Exports all globals by default
  Exports only global listed is "globals" used
  Exports no global if "globals" listed alone
Full Objects
  Exports all objects by default
  Exports only objects listed if "object" used
  Exports no object if "object" listed alone
Read-only (export only)
  Globals and objects

## Slide 127: Event handlers
Init – initialization function
on_init ...; ans=status;
  status is GLD_OK or GLD_ERROR
Sync – synchronization function
on_sync ...; ans=result;
  result must be a timestamp (second of epoch) or
    TS_NEVER – no event expected
    TS_ERROR – an error occurred and simulation should stop
Term – termination function
on_term ...; ans=status;

## Slide 128: Other link directives
workdir folder
  Sets the working folder for Matlab
window status
  Controls status of Matlab window (e.g., hide, show, keep)
  Tip: use show and type in "workspace" to see the workspace
output size
  Sets the buffer size for the answer value

## Slide 129: Building GridLAB-D to support Matlab
./configure --with-matlab=<matlab-path>
Notes:
  Multiple versions of Matlab are often present on a system; please make sure your search PATH matches the path specified in "configure"
  Built-in Matlab support is flagged using "MATLAB" global
  Validation must be explicitly enabled by removing "validate.no" from gldcore/link/matlab folder
  Validation test are important to ensuring link works ok
  Check the forums if you have trouble, you're probably not the first to encounter a particular problem

## Slide 130: Realtime Simulation

## Slide 131: GridLAB-D in realtime
Main simulation
System Clock
Model clock
Data
Access
Server
Web
Browser
Emulators
Hardware
MySQL
Database

## Slide 132: Realtime mode
Realtime operation: "run_realtime" global variable
  Non-zero  simulation clock tied to system clock
  Defines the system clock factor (default is 1.0)
Command line control
  host% gridlabd -D run_realtime=1 mymodel.glm
Caveats:
  Cannot be used with DELTAMODE (subsecond dynamics)
  Realtime loading cannot exceed 1.0 (see realtime_metric)

## Slide 133: Server mode
Allows direct global and object data access over TCP
  Enabled by --server command-line option, or in GLM file: #option server;
  Supports multiple protocols (raw, json, XML)
  Default TCP port is 6267 (see server_portnum)
Caveat:
  Independent server thread  asynchronous data access
    Possible to access data during an update (known issue)
    Probability of occurrence is given by 1-realtime_metric
    Typical value of realtime_metric > 0.99

## Slide 134: Reading/writing global values
Query format:
    http://hostname:port/protocol/variable-name
    - or -
    http://hostname:port/protocol/variable-name=value
Result format depends on protocol
  Get query returns current value
  Set query returns previous value
Caveats
  Globals do not support unit conversion (known issue)
  Writing some globals can cause erroneous results

## Slide 135: Reading/writing object data
Query format:
    http://hostname:port/protocol/object/*
    http://hostname:port/protocol/object/property
    http://hostname:port/protocol/object/property[unit]
    http://hostname:port/protocol/object/property=value
Features/caveats
  "*" returns all properties of an object (json and XML only)
  Value may always include units, e.g., temp=64 degF
  Read units are only supported in

## Slide 136: XML formatting
Special unit formatting for double and complex values
  property-name[unit,precision format part]
  Unit may be any valid simple or compound unit
  Precision is a single digit from 0 to 9 for the mantissa size
  Format may be any valid printf double format character (e.g., one of "aAeEfFgG")
  Part indicated complex number computation to use
    i, j, d, r for complex formatting in rectangular or polar form
    M,D,R for magnitude only, or angle only (degrees or radians)
    X,Y for real and imaginary parts only

## Slide 137: Runtime file access
GridLAB-D files accessible with runtime rewrite
  Query format: http://hostname:port/rt/filename
Substitutes occurrences of <<<global-variable>>>
  Example:
  http://<<<hostname>>>:<<<server_portnum>>>/rt/page.htm becomes http://localhost:6267/rt/page.htm

## Slide 138: Javascript API for HTML files (read)
Requires Javascript runtime in HTML file
  <SCRIPT src="gridlabd.js"></SCRIPT>
Allows update of <DIV> fields in HTML documents
Example (read):
  <BODY ONLOAD="refresh();">
  <SCRIPT src="gridlabd.js"></SCRIPT>
  <DIV ID="verbose">...</DIV>
  <SCRIPT type="text/javascript">
  function refresh()
  {
  document.getElementById("verbose").innerHTML
  = GLDGetGlobal("verbose");
  }
  </SCRIPT>

## Slide 139: Javascript API for HTML files (write)
Example (write):
  <INPUT TYPE="submit"
  VALUE="Off"
  ONCLICK="GLDSetGlobal('verbose',0);"
  />
  <INPUT TYPE="submit"
  VALUE="On"
  ONCLICK="GLDSetGlobal('verbose',1);"
  />

## Slide 140: IEEE123 Realtime Simulation Demo
Private github project for collaborators:
  http://github.com/dchassin/ieee123
Support four concurrent realtime simulations
  Running as a RHEL6 system service using gridlabd-ctl
  Includes feeder control interface with Google Earth mapping
  All data is recorded in a MySQL database
  Outputs SCADA, AMI, and complete model for variants
    ieee123z – static loads, no solar panels
    ieee123 – dynamic loads, no solar panels
    ieee123s – dynamic loads with solar panels
    ieee123sz – static loads with solar panels
Historical runs
  Full simulations of history supported for forecast calibration

## Slide 141: Runtime Classes

## Slide 142: Runtime class: an "on-the-fly" module
GLM File
C code
DLL
GridLAB-D

## Slide 143: GridLAB-D Core Solver
Update order by "ranks"
  Loader sets initial ranks
  Modules adjust ranks
Each time-step may iterate
  Precommit
  Presync/sync/postsync
    PLC and recalc on all syncs
  Commit
Valid_to sub-sync events
  Sync without return to main

## Slide 144: Presync iteration process
Source: S. Jin and D.P. Chassin, "Thread Group Multithreading: Accelerating the computation of an Agent-based Power System Modeling and Simulation Tool – GridLAB-D," 2014 Hawaii International Conference on System Science (HICSS-48), 2014.

## Slide 145: Sync iteration process
Source: S. Jin and D.P. Chassin, "Thread Group Multithreading: Accelerating the computation of an Agent-based Power System Modeling and Simulation Tool – GridLAB-D," 2014 Hawaii International Conference on System Science (HICSS-48), 2014.

## Slide 146: Postsync interation process
postsync()
postsync()
postsync()
postsync()
Source: S. Jin and D.P. Chassin, "Thread Group Multithreading: Accelerating the computation of an Agent-based Power System Modeling and Simulation Tool – GridLAB-D," 2014 Hawaii International Conference on System Science (HICSS-48), 2014.

## Slide 147: Definition of runtime classes
Augmented class definition:
  Must include at least one "intrinsic" declaration
  intrinsic create(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic init(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic precommit(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic presync(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic sync(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic postsync(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic recalc(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic notify(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic plc(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic isa(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic commit(TIMESTAMP t0, TIMESTAMP t1) { ... };
  intrinsic finalize(TIMESTAMP t0, TIMESTAMP t1) { ... };

## Slide 148: Intrinsic functions
All functions return int64 (some as TIMESTAMP)
  create int64 0=failure, 1=success
  init int64 0=failure, 1=success
  precommit int64 0=failure, 1=success
  presync TIMESTAMP <t1=stop, t1: iterate, >t1: success
  sync TIMESTAMP <t1=stop, t1: iterate, >t1: success
  postsync TIMESTAMP <t1=stop, t1: iterate, >t1: success
  recalc int64 0=failure; 1=success
  notify int64 0=failure; 1=success
  plc TIMESTAMP <t1=stop, t1: iterate, >t1: success
  isa int64 0=no; 1=yes
  commit TIMESTAMP <t1=stop, t1: iterate, >t1: success
  finalize int64 0=failure; 1=success

## Slide 149: Example: thermostat redesign
Heater
House
+
+
QD
–
TS
TA
e
m
Qh
Q
Conventional analog thermostat:
Discrete-time zero-deadband thermostat:
Heater
House
+
+
QD
–
TS
TA
e
m
Qh
Q
ts
ZOH

## Slide 150: Discrete-time control thermostat
Simple zero-deadband digital heating thermostat
  No deadband
  Discrete-time thermostat (ts = 5 minutes)
  Basis for "transactive" thermostats
Class declaration:
class new_thermostat {
double Tair;
double Theat;
int64 mode;
intrinsic presync(TIMESTAMP t0, TIMESTAMP t1) { ... };
}

## Slide 151: Simple heating thermostat
intrinsic presync(TIMESTAMP t0, TIMESTAMP t1)
{
// get the setpoint and air temperatures
gl_get_value(my->parent,"heating_setpoint",Theat);
gl_get_value(my->parent,"air_temperature",Tair);
// typedefs for mode and control status
typedef enum {SM_OFF=1, SM_HEAT=2} MODE;
typedef enum {SM_NONE=2} TSTAT;
if ( t1%300 == 0 ) // time to update
{
// disable house's internal thermostat
*(TSTAT*)gl_get_addr(my->parent,"thermostat_control") = SM_NONE;
// compute the new mode
mode = ( Tair < Theat ) ? SM_HEAT : SM_OFF;
// send new mode to the house
*(MODE*)gl_get_addr(my->parent,"system_mode") = mode;
}
return ((t1/300)+1)*300; // next update time
}

## Slide 152: Contact information
This document is available at
http://github.com/dchassin/tutorial/Short-courses/UCB 2016-10-21.pptx
dchassin@slac.stanford.edu